## Slide 1
1
2
3
4
5
Notes: (2 min)
Optical systems are composed of three elementary blocks: A source that radiates light, a sample through which light propagates, and a detector that measures the light. All optical systems have variations of this setup.
[click] Sources can be individual LEDs or lasers. Or you can use an array of LEDs and lasers at different locations. Or you can use digital micromirrors (array of toggles) to manipulate the LED or laser light to project patterns.
[click] Analogously, you have detectors that measure light. You can have single photodiodes, or have them connected in an array. Cameras do a similar thing—they capture light through a small lens using a tiny array of microscopic detectors.
[click] So what happens as light goes through this media?
[click] Light can reflect off the surface of the tissue. The index of refraction can be used to determine how much the path of light is bent as it transitions from one medium to another.
[click] If a photon enters the turbid media, it can be absorbed (depending on the component concentrations of the media).
  In NIR range, things like water, hemoglobin, and lipids are the main absorption components.
  And we use the value of mua, the inverse of the average path length traveled prior to being absorbed, as the metric.
Light can also scatter as it enters.
  [click] It can scatter and then be absorbed
  [click] It can scatter and exit the medium (and if we place a detector there, then we can detect it)
  [click] And it can scatter and make its back to the surface from which it entered.
  [click] And we use the value of mus, the inverse of the distance between scattering events, as the metric.
    We also use mus’, which accounts for the forward motion of photons. Mus’ describes the inverse length at which the directionality of the photon propagation in tissue has been randomized due to multiple scattering events.
Why is this important?!
Well, the measured light, in combination with the known type of source, allows for the determination of biological structure and function of the tissue is just went through.
---------
For example, we can determine concentration of hemoglobine in tissue from particular wavelengths.
From this, we can infer parameters such as total hemoglobin concentration (𝑇𝐻𝐶=𝐻𝑏𝑅+𝐻𝑏𝑂_2) and tissue oxygen saturation (𝑆〖𝑡𝑂〗_2= 〖𝐻𝑏𝑂_2〗∕〖(𝐻𝑏𝑅+ 𝐻𝑏𝑂_2)〗)

## Slide 2
Print square wall with settings
Set settings: EM=1 PW=0.4
Measure Path Width
Does the path width
= 0.4 mm?
Done
No
Yes